# 🛠️ SALAR Pre-processing Suite
This directory contains the essential tools required to bridge the gap between raw hardware acquisition and the SALAR Analysis Core. These utilities ensure that data from various sources is standardized, noise-filtered, and formatted correctly for electrophysiological mapping.
## 📂 Included Utilities
### 1. Video-to-Frame Converter
This is the primary gateway for data captured in standard video containers (AVI/MP4).
- Template-Driven: Includes pre-defined rules for the Casio EX-ZR1200, automatically handling the specific resolution and frame-rate combinations used in high-speed research (e.g., 120Hz to 1000Hz).
- Data Integrity: Extracts frames to raw formats (BMP/TIFF) to ensure no further compression loss occurs before signal analysis.
- Scientific Benchmarking: Used to extract the frame sequences from the Nature (Scientific Reports) benchmark datasets.
### 2. ROI & Signal Optimizer
A set of tools for preparing the extracted frames:
- Spatial Cropping: Focus on the cardiac tissue area to reduce processing time and memory overhead.
- Intensity Normalization: Adjusts signal levels to ensure consistent thresholding for APD80 detection.

## ⚠️ Dependencies & Compilation
### TVideoGrabber Requirement
The Video-to-Frame Converter utilizes the TVideoGrabber (Datastead) SDK for low-level video stream handling.
- Note: The commercial units/DLLs for TVideoGrabber are not included in this repository.
- To compile this tool, you must have a valid TVideoGrabber license installed in your Delphi environment.
- Independent Core: Please note that the main SALAR Analysis Core (APD/CV mapping) does not require this dependency and can be used with any raw image sequence.

## 🚀 How to Use
1. Acquisition: Capture your data using the FLIR Blackfly S utility or a high-speed camera like the Casio EX-ZR1200.
2. Conversion: Run the Converter tool, select your hardware template, and point it to your video file.
3. Output: The tool will generate a numbered sequence of frames in a dedicated folder.
4. Next Step: Load this folder into the SALAR Core for signal processing.